## Slide 1: Experiment

## Slide 2: 1. Safety
Some basic safety rules
Wear safety goggles
When diluting an acid, always add the acid to water.
Always work with good ventilation通风设备.
When heating substance, do it slowly.

## Slide 3: 2. Accuracy 准确度
Some rules for ensuring the accuracy of experimental results:
When titrating, rinse the buret/burette （润洗滴定管）with solution to be used in the titration instead of water.
Don’t contaminate your chemicals.
Be conscious of significant figures.

## Slide 4: accuracy 准确度& precision精确度

## Slide 5: 3. Significant Figures有效数字

## Slide 7: 4. Method of Separation
过滤

## Slide 8
4. Method of Separation
蒸馏

## Slide 9
4. Method of Separation

## Slide 10: 5. Titration滴定

## Slide 11: 6. Laboratory Equipment
Beaker 烧杯
Buret滴定管
Burner喷灯
Crucible tongs坩埚钳
Dropper pipette滴管
Erlenmeyer flask锥形瓶
Evaporating dish蒸发皿
Florence flask 平底烧瓶

## Slide 12: 6.Laboratory Equipment
Forceps 镊子
Funnel漏斗
Graduated cylinder量筒
Rubber policeman 橡胶淀帚
Safty goggles护目镜
Test tube试管
Thermometer温度计
Condenser pipe冷凝管

## Slide 13: 6.Laboratory Equipment
Graduated pipette移液管
Volumetric pipette容量移液管
Mortar and pestle研钵和研杵
Pipette bulb洗耳球
Platform balance天平
Ring clamp 铁圈

## Slide 14
2、原理：
HCl+NaOH=NaCl+H2O
C1V1=C2V2
C1＝
C2V2
V1
1、定义：
酸碱中和滴定
用已知浓度的酸（或碱）测定未知浓度的碱（或酸）浓度的方法叫酸碱中和滴定。
  *已知浓度的溶液——标准液
  *未知浓度的溶液——待测液
Titration

## Slide 15: 3、实验仪器
Buret
类型:酸式滴定管和碱式滴定管
标识:标有温度、规格、刻度 （“0”刻度在最高点，上下部各有一段无刻度）最小分刻度：0.1mL，读数精确到0.01mL

## Slide 16
0 10 20 30 40 V(NaOH)mL
12 10 8 6 4 2
PH
颜色突变范围
4.中和滴定曲线
酚酞
甲基橙

## Slide 17: 5、指示剂的选择及滴定终点的判断
（1）指示剂
甲基橙 3.1-4.4 红－橙－黄
酚酞 8-10 无－粉红
（2）滴定终点的判断
指示剂的颜色发生突变并且半分钟不变色即达到滴定终点，终点的判断是滴定实验是否成功的关键。
原则：浅入深

## Slide 18: 6、滴定管的使用准备
(1)检查是否漏水
(2)洗涤：先水洗，再用待装液润洗2-3次
(3)排气泡，调液面：先装入液体至“0”刻度以上2-3厘米处，排净气泡后调整液面到“0”或“0”以下，平视记下刻度，

## Slide 19
7、实验步骤
(1)查漏
滴定管是否漏水、旋塞转动是否灵活
(2)洗涤
滴定管：
用蒸馏水洗→然后用待装液润洗2～3次。
锥形瓶：
蒸馏水清洗2~3次（不能用待盛液润洗）

## Slide 20: (3)装液
滴定管中装入待测液→挤气泡→调液面→记下起始读数→放液至锥形瓶→记录终点读数→滴入指示剂
滴定管中装入标准液→挤气泡→调液面→记下起始读数

## Slide 21
(4)滴定
右手持锥形瓶颈部，向同一方向作圆周运动
. 左手控制活塞（或玻璃球）
滴加速度先快后慢
视线注视锥形瓶中溶液颜色变化
. 指示剂变色后，半分钟颜色不变，到达滴定终点，再读数。
.复滴2~3次，记录数据。

## Slide 22
(4)滴定
右手持锥形瓶颈部，向同一方向作圆周运动
. 左手控制活塞（或玻璃球）
滴加速度先快后慢
视线注视锥形瓶中溶液颜色变化
. 指示剂变色后，半分钟颜色不变，到达滴定终点，再读数。
.复滴2~3次，记录数据。

## Slide 23
实验：用0.10mol/L的NaOH溶液滴定稀盐酸
(1)查漏
(2)洗涤（滴定管，锥形瓶，润洗）
(3)装液（待测液，标准液，指示剂）
(4)滴定
右手持锥形瓶颈部，向同一方向作圆周运动
左手控制活塞（或玻璃球）
滴加速度先快后慢
视线注视锥形瓶中溶液颜色变化
指示剂变色后，半分钟颜色不变，到达滴定终点，
再读数。
复滴2-3次，记录数据。